## Slide 1
General approach:
A: action
S: pose
O: observation
Position at time t depends on position previous position and action, and current observation

## Slide 2
Uniform Prior
Observation: see pillar
Action: move right
Observation: see pillar

## Slide 3: Example
P(z|open) = 0.6 P(z|open) = 0.3
P(open) = P(open) = 0.5
P(open | z) = ?

## Slide 4: Example
P(z|open) = 0.6 P(z|open) = 0.3
P(open) = P(open) = 0.5
raises the probability that the door is open.

## Slide 5: Example: 2nd Measurement
P(z2|open) = 0.5 P(z2|open) = 0.6
P(open|z1)=2/3
lowers the probability that the door is open.

## Slide 6
for :
If the door is open, the action “close door” succeeds in 90% of all cases.

## Slide 7: Example: The Resulting Belief

## Slide 8: Example: The Resulting Belief
OK… but then what’s the chance that it’s still open?

## Slide 9: Example: The Resulting Belief

## Slide 10: Summary
Bayes rule allows us to compute probabilities that are hard to assess otherwise.
Under the Markov assumption, recursive Bayesian updating can be used to efficiently combine evidence.

## Slide 11: Example

## Slide 12: Example
s
P(s)

## Slide 13: Example

## Slide 14: Example
How does the probability distribution change if the robot now senses a wall?

## Slide 15: Example 2
0.2 | 0.2 | 0.2 | 0.2 | 0.2

## Slide 16: Example 2
0.2 | 0.2 | 0.2 | 0.2 | 0.2
Robot senses yellow.
Probability should go up.
Probability should go down.

## Slide 17: Example 2
States that match observation
  Multiply prior by 0.6
States that don’t match observation
  Multiply prior by 0.2
0.2 | 0.2 | 0.2 | 0.2 | 0.2
Robot senses yellow.
0.04 | 0.12 | 0.12 | 0.04 | 0.04

## Slide 18: Example 2
!
The probability distribution no longer sums to 1!
0.04 | 0.12 | 0.12 | 0.04 | 0.04
Normalize (divide by total)
.111 | .333 | .333 | .111 | .111
Sums to 0.36

## Slide 19: Nondeterministic Robot Motion
R
The robot can now move Left and Right.
.111 | .333 | .333 | .111 | .111

## Slide 20: Nondeterministic Robot Motion
R
The robot can now move Left and Right.
.111 | .333 | .333 | .111 | .111
When executing “move x steps to right” or left:
.8: move x steps
.1: move x-1 steps
.1: move x+1 steps

## Slide 21: Nondeterministic Robot Motion
Right 2
The robot can now move Left and Right.
0 | 1 | 0 | 0 | 0
0 | 0 | 0.1 | 0.8 | 0.1
When executing “move x steps to right”:
.8: move x steps
.1: move x-1 steps
.1: move x+1 steps

## Slide 22: Nondeterministic Robot Motion
Right 2
The robot can now move Left and Right.
0 | 0.5 | 0 | 0.5 | 0
0.4 | 0.05 | 0.05 | 0.4 | (0.05+0.05) 0.1
When executing “move x steps to right”:
.8: move x steps
.1: move x-1 steps
.1: move x+1 steps

## Slide 23: Nondeterministic Robot Motion
What is the probability distribution after 1000 moves?
0 | 0.5 | 0 | 0.5 | 0

## Slide 24: Example

## Slide 25: Example
Right

## Slide 26: Example

## Slide 27: Example
Right

## Slide 28: Kalman Filter Model
Area under the curve sums to
Gaussian
(in for now)
σ2

## Slide 29: Kalman Filter
Sense
Move
Initial Belief
Gain Information
Lose
Information
Bayes Rule
(Multiplication)
Convolution
(Addition)
Gaussian:
μ, σ2

## Slide 30: Measurement Example
Prior Position Estimate
Measurement Estimate
μ, σ2
v, r2

## Slide 31: Measurement Example
Prior Position Estimate
Measurement Estimate
Where is the new mean ?
μ, σ2
v, r2

## Slide 32: Measurement Example
Prior Position Estimate
Measurement Estimate
What is the new covarance ?
μ, σ2
v, r2
σ2’?

## Slide 33: Measurement Example
Prior Position Estimate
Measurement Estimate
New Estimate
μ, σ2
v, r2
μ', σ2’
To calculate, go through and multiply the two Gaussians and renormalize to sum to 1
Also, the multiplication of two Gaussian random variables is itself a Gaussian

## Slide 34: Multiplying Two Gaussians
(ignoring the constant term in front)
To find the mean, need to maximize this function (i.e. take derivative)
Set equal to and solve for
…something similar for the variance
Prior Position Estimate
Measurement Estimate
μ, σ2
v, r2
(ignoring constant term in front)
To find mean, maximize function (i.e., take derivative)
4. Set equal to 0 and solve for x
… something similar for the variance:

## Slide 35: Another point of view…
Prior Position Estimate
Measurement Estimate
New Estimate
μ, σ2
v, r2
μ', σ2’
: p(x)
: p(z|x)
: p(x|z)

## Slide 36: Example
Prior Position Estimate
Measurement Estimate

## Slide 37: Example
Prior Position Estimate
Measurement Estimate
Notes: Sigma2 = 16*16 / (16+16) = 256/32 = 8 -> 2.83
u=(10*16+12*16)/(16+16))=(160+192)/32)=11

## Slide 38: Example
Prior Position Estimate
Measurement Estimate
μ’=12.4
σ2’=1.6

## Slide 39: Kalman Filter
Sense
Move
Initial Belief
Lose
Information
Convolution
(Addition)
Gaussian:
μ, σ2

## Slide 40: Motion Update
For motion
Model of motion noise
μ’=μ+u
σ2’=σ2+r2
u, r2

## Slide 41: Motion Update
For motion
Model of motion noise
μ’=μ+u
σ2’=σ2+r2
u, r2
Prior Position Estimate
M

## Slide 42: Motion Update
For motion
Model of motion noise
μ’=μ+u=18
σ2’=σ2+r2=10
u, r2
Prior Position Estimate
M

## Slide 43: Kalman Filter
Sense
Move
Initial Belief
Gaussian:
μ, σ2
μ’=μ+u
σ2’=σ2+r2

## Slide 44: Kalman Filter in Multiple Dimensions
2D Gaussian

## Slide 45: Implementing a Kalman Filter example
VERY simple model of robot movement:
What information do our sensors give us?

## Slide 46: Implementing a Kalman Filter example
H = [1 0]
F
H

## Slide 47: Implementing a Kalman Filter
Estimate
P’ uncertainty covariance
F state transition matrix
u motion vector
F motion noise
Measurement
measurement function
measurement noise
identity matrix

## Slide 48: Particle Filter Localization (using sonar)
http://www.cs.washington.edu/ai/Mobile_Robotics//mcl/animations/global-floor-start.gif

## Slide 49: Particles
Each particle is a guess about where the robot might be
x
y
θ

## Slide 50: Robot Motion
move each particle according to the rules of motion
+
add random noise
particles
particles

## Slide 51: Incorporating Sensing

## Slide 52: Incorporating Sensing
Difference between the
actual measurement
and the
estimated measurement
Importance weight

## Slide 53: Importance weight python code
def Gaussian(self, mu, sigma, x):
# calculates the probability of x for 1-dim Gaussian with mean mu and var. sigma
return exp(- ((mu - x) ** 2) / (sigma ** 2) / 2.0) / sqrt(2.0 * pi * (sigma ** 2))
def measurement_prob(self, measurement):
# calculates how likely a measurement should be
prob = 1.0;
for i in range(len(landmarks)):
dist = sqrt((self.x - landmarks[i][0]) ** 2 + (self.y - landmarks[i][1]) ** 2)
prob *= self.Gaussian(dist, self.sense_noise, measurement[i])
return prob
def get_weights(self):
w = []
for i in range(N): #for each particle
w.append(p[i].measurement_prob(Z)) #set it’s weight to p(measurement Z)
return w

## Slide 54: Importance weight pseudocode
Calculate the probability of a sensor measurement for a particle:
prob = 1.0;
for each landmark
d = Euclidean distance to landmark
prob *= Gaussian probability of obtaining a reading at
distance d for this landmark from this particle
return prob

## Slide 55: Incorporating Sensing

## Slide 56: Resampling
original particles
Importance Weight |  | 
0.2 |  | 
0.6 |  | 
0.2 |  | 
0.8 |  | 
0.8 |  | 
0.2 |  | 
Sum is 2.8

## Slide 57: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8

## Slide 58: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement

## Slide 59: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement
Is it possible that one of the particles is never chosen?
Yes!
Is it possible that one of the particles is chosen more than once?
Yes!

## Slide 60: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement
What is the probability that this particle is not chosen during the resampling of the six new particles?
Notes: .71 ^ 6 = 12.8%

## Slide 61: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement
What is the probability that this particle is not chosen during the resampling of the six new particles?

## Slide 62: Question
What happens if there are no particles near the correct robot location?

## Slide 63: Question
What happens if there are no particles near the correct robot location?
Possible solutions:
  Add random points each cycle
  Add random points each cycle, where is proportional to the average measurement error
  Add points each cycle, located in states with a high likelihood for the current observations

## Slide 64: Summary
Kalman Filter
  Continuous
  Unimodal
  Harder to implement
  More efficient
  Requires a good starting guess of robot location
Particle Filter
  Continuous
  Multimodal
  Easier to implement
  Less efficient
  Does not require an accurate prior estimate