## Slide 1: EE434: ASIC and Digital Systems
Midterm Review 1
Jacob Murray
School of EECS, WSU
jmurray@eecs.wsu.edu

## Slide 2: Structure of the Exam
Four problems with multiple parts
All topics will be almost equally represented
Will look similar to layout of sample exam

## Slide 3: Overview
Circuit Design Methodologies
Implementation Techniques
RTL Design and Synthesis

## Slide 4: Circuit Design Methodology
Static CMOS
Pseudo NMOS
Pass-transistor
Transmission Gate
Domino Logic

## Slide 5: Gate Capacitance
Cut-off
Resistive
Saturation

## Slide 6: Threshold Drops
VDD
VDD  0
PDN
0  VDD
CL
CL
PUN
VDD
0  VDD - VTn
CL
VDD
VDD
VDD  |VTp|
CL
S
D
S
D
VGS
S
S
D
D
VGS
Notes: Why PMOS in PUN and NMOS in PDN … threshold drop
NMOS transistors produce strong zeros; PMOS transistors generate strong ones

## Slide 7: Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
Notes: Shown synthesis of pull up from pull down structure

## Slide 8: Constructing a Complex Gate

## Slide 9: Basic CMOS Gate Sizing
NAND and NOR gate sizing

## Slide 10: Issues with Pass Transistor Logic
Threshold drop
Capacitive feed through
Charge sharing

## Slide 11: NMOS Only Logic: Level Restoring Transistor
M
2
M
1
M
n
M
r
Out
A
B
V
DD
V
DD
Level Restorer
X
• Advantage: Full Swing
• Restorer adds capacitance, takes away pull down current at X
• Ratio problem

## Slide 12: Complementary Pass Transistor Logic

## Slide 13: Transmission Gate
A
B
C
C
A
B
C
C
B
C
L
C
= 0 V
A =
2.5 V
C =
2.5 V

## Slide 14: Pass-Transistor Based Multiplexer
The control signal S turns the transfer gates on and off depending on its value.
When S=1, the upper transfer gate is on and output follows
When S=0, the lower transfer gate is on and output follows
Exercise: Implement the Multiplexer with static CMOS and compare with this

## Slide 15: Dynamic Gate
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out
CL
Out
Clk
Clk
A
B
C
Mp
Me
Two phase operation
Precharge (Clk = 0)
Evaluate (Clk = 1)
off
off
1
on
on
((AB)+C)
Notes: For lecture
Evaluate transistor, Me, eliminates static power consumption

## Slide 16: Conditions on Output
Once the output of a dynamic gate is discharged, it cannot be charged again until the next precharge operation.
Inputs to the gate can make at most one transition during evaluation.
Output can be in the high impedance state during and after evaluation (PDN off), state is stored on CL
This behavior is fundamentally different than the static counterpart that always has a low resistance path between the output and one of the power rails.
Notes: This behavior is fundamentally different than the static counterpart that always has a low resistance path between the output and one of the power rails.

## Slide 17: Properties of Dynamic Gates
Logic function is implemented by the PDN only
  number of transistors is N + 2 (versus 2N for static complementary CMOS)
Full swing outputs
Non-ratioed - sizing of the devices does not affect the logic levels
Faster switching speeds
  reduced load capacitance due to lower input capacitance (Cin)
  reduced load capacitance due to smaller output loading (Cout)
Notes: CL being lower also contributes to power savings

## Slide 18: Properties of Dynamic Gates
Overall power dissipation usually higher than static CMOS
  no static current path ever exists between VDD and GND
  no glitching
  higher transition probabilities
  extra load on Clk
Needs a precharge/evaluate clock

## Slide 19: Issues in Dynamic Design 1: Charge Leakage
CL
Clk
Clk
Out
A
Mp
Me
Leakage sources
CLK
VOut
Precharge
Evaluate
Leakage sources are reverse-biased diode and the sub-threshold leakage of the NMOS pull down device.
Notes: leakage sources are reverse-biased diode and the sub-threshold leakage of the NMOS pull-down device.
Charge stored on CL will leak away with time (input in low state during evaluation)
Requires a minimum clock rate - so not good for low performance products such as watches (or when have conditional clocks)
PMOS precharge device also contributes some leakage due to reverse bias diode and subthreshold conduction that, to some extent, offsets the leakage due to the pull down paths.

## Slide 20: Solution to Charge Leakage
CL
Clk
Clk
Me
Mp
A
B
Out
Mkp
Same approach as level restorer for pass-transistor logic
During precharge, Out is VDD and inverter out is GND, so keeper is on
Keeper
Notes: During precharge, Out is VDD and inverter out is GND, so keeper is on
During evaluation if PDN is off, the keeper compensates for drained charge due to leakage.
If PDN is on, there is a fight between the PDN and the PUN - circuit is ratioed so PDN wins, eventually
Note Psc during switching period when PDN and keeper are both on simultaneously

## Slide 21: Issues in Dynamic Design 2: Charge Sharing
Initially, CA discharged and CL fully charged
Charge stored originally on CL is redistributed (shared) over CL and CA leading to reduced robustness
CL
Clk
Clk
CA
CB
B=0
A
Out
Mp
Me
Notes: CA initially discharged and CL fully charged.

## Slide 22: Solution to Charge Redistribution
Clk
Clk
Me
Mp
A
B
Out
Mkp
Clk
Precharge internal nodes using a clock-driven transistor (at the cost of increased area and power)

## Slide 23: Issues in Dynamic Design 3: Clock Feedthrough (Charge Injection)
CL
Clk
Clk
B
A
Out
Mp
Me
Coupling between Out and Clk input of the precharge device due to the gate to drain capacitance. So voltage of Out can rise above VDD. The fast rising (and falling edges) of the clock couple to Out.
Notes: Danger is that signal levels can rise enough above VDD that the normally reverse-biased junction diodes become forward-biased causing electrons to be injected into the substrate.

## Slide 24: Clock Feedthrough
Clk
Clk
In1
In2
In3
In4
Out
In &
Clk
Out
Time, ns
Voltage
Clock feedthrough
Clock feedthrough

## Slide 25: Cascading Dynamic Gates
Clk
Clk
Out1
In
Mp
Me
Mp
Me
Clk
Clk
Out2
V
t
Clk
In
Out1
Out2
V
VTn
Only 0  1 transitions allowed at inputs!
Notes: Out2 should remain at VDD since Out1 transitions to 0 during evaluation. However, since there is a finite propagation delay for the input to discharge Out1 to GND, the second output also starts to discharge.
The second dynamic inverter turns off (PDN) when Out1 reaches VTn.
Setting all inputs of the second gate to 0 during precharge will fix it.
Correct operation is guaranteed (ignoring charge redistribution and leakage) as long as the inputs can only make a single 0 -> 1 transition during the evaluation period

## Slide 26: Cascading Dynamic Gates
Out2 should remain at VDD since Out1 transitions to 0 during evaluation. However, since there is a finite propagation delay for the input to discharge Out1 to GND, the second output also starts to discharge.
The second dynamic inverter turns off (PDN) when Out1 reaches VTn.
Setting all inputs of the second gate to 0 during precharge will fix it.
Correct operation is guaranteed (ignoring charge redistribution and leakage) as long as the inputs can only make a single 0 → 1 transition during the evaluation period

## Slide 27: Domino Logic
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PDN
In5
Me
Mp
Clk
Clk
Out2
Mkp
1  1
1  0
0  0
0  1
Ensures all inputs to the Domino gate are set to 0 at the end of the precharge period. Hence, the only possible transition during evaluation is 0 → 1
Notes: Ensures all inputs to the Domino gate are set to 0 at the end of the precharge period. Hence, the only possible transition during evaluation is 0 -> 1

## Slide 28: Why Domino?
Clk
Clk
Ini
PDN
Inj
Ini
Inj
PDN
Ini
PDN
Inj
Ini
PDN
Inj
Like falling dominos!

## Slide 29: Properties of Domino Logic
Only non-inverting logic can be implemented
Very high speed
  static inverter can be skewed, only 0 → 1 transition
  Input capacitance reduced
Notes: First 32 bit micro (BellMAC 32) was designed in Domino logic
Now a rather rare design style due to non-inverting logic only

## Slide 30: Differential (Dual Rail) Domino
A
B
Me
Mp
Clk
Clk
Out = AB
!A
!B
Mkp
Clk
Out = AB
Mkp
Mp
Solves the problem of non-inverting logic
1 0
1 0
on
off
Notes: AND/NAND differential logic gate. The inputs and their complements come from other differential DR gates and thus all inputs are low during precharge and make a conditional transition from 0 to 1.
Annotations show state during evaluate cycle (CLK = 1)
Expensive - but can implement any arbitrary function.
Use significant power since they have a guaranteed transition every single clock cycle (regardless of signal statistics, since either Out or !Out will transition from 0 to 1).
Not ratioed (even though have a cross-coupled PMOS pair)

## Slide 31: Sequential Circuits
Difference between latch and flip-flops
Design of latches and flip-flops using transmission gates
Different Design trade-offs
Role of non-overlapping clocks

## Slide 32: Timing Definitions
t
CLK
t
D
t
c
2
q
t
hold
t
su
t
Q
DATA
STABLE
DATA
STABLE
Register
CLK
D
Q

## Slide 33: Storage Mechanisms
D
CLK
CLK
Q
Dynamic
Static
Needs a positive feedback loop to hold the data
Holds data by storing charge on capacitance

## Slide 34: Implementation Methodology
Different digital circuit design methodologies
  Custom, semi-custom, array-based
Characteristics of CPLDs and FPGAs
Implementation of logic functions using MUX and LUTs
Hard and Soft Macro

## Slide 35: Array-Based Programmable Logic
PLA
PROM
PAL
I
5
I
4
O
0
I
3
I
2
I
1
I
0
O
1
O
2
O
3
Programmable AND array
Programmable
OR array
I
5
I
4
O
0
I
3
I
2
I
1
I
0
O
1
O
2
O
3
Programmable AND array
Fixed OR array
Indicates programmable connection
Indicates fixed connection
O
0
I
3
I
2
I
1
I
0
O
1
O
2
O
3
Fixed AND array
Programmable
OR array

## Slide 36: Implementing functions with PLA

## Slide 37: Programming a PROM
f
0
1
X
2
X
1
X
0
f
1
NA
NA
: programmed node

## Slide 38: 2-input MUX as programmable logic block
F
A
0
B
S
1
Configuration
A
B
S
F=
0
0
0
0
0
X
1
X
0
Y
1
Y
0
Y
X
XY
X
0
Y
Y
0
X
Y
1
X
X
+
Y
1
0
X
1
0
Y
1
1
1
1
XY
XY
X
Y

## Slide 39: Two-input LUT

## Slide 40: Elmore Delay

## Slide 41: Delay of a wire

## Slide 42: Clock Design Issues

## Slide 43: Reducing Power in Clocking
Gated Clocks:
  can gate clock signals through AND gate before applying to flip-flop; this is more of a total chip power savings
  all clock trees should have the same type of gating whether they are used or not, and at the same level - total balance
Reduce overall capacitance (again, shielding vs. spacing)
(a) higher total cap./less area (b) lower cap./ more area
  Tradeoff between the two approaches due to coupling noise
  approach (a) is better for inductive noise; (b) is better for capacitive noise
shield
clock
shield
Signal 1
clock
Signal 2

## Slide 44: VHDL
You will NOT need to write any long complicated code
You should be able to write small pieces of VHDL
Understand common coding mistakes
Understand process and sensitivity list
Be able to detect limitations in a block of code