## Slide 1: Execution of Multiple Instructions per cycle

## Slide 2: Getting CPI < 1: Issuing Multiple Instructions/Cycle
Two variations
  Superscalar: varying number of instructions/cycle (1 to 8), scheduled by compiler or by HW (Tomasulo)
    IBM PowerPC, Sun UltraSparc, DEC Alpha, HP 8000
  (Very) Long Instruction Words (V)LIW: fixed number of instructions (4-16) scheduled by the compiler; put ops into wide templates
    Joint HP/Intel agreement in 1999/2000
    Intel Architecture-64 (IA-64) 64-bit address
    Style: “Explicitly Parallel Instruction Computer (EPIC)”
Anticipated success lead to use of Instructions Per Clock cycle (IPC) vs. CPI

## Slide 3: Getting CPI < 1: Issuing Multiple Instructions/Cycle
Superscalar DLX: 2 instructions, 1 FP & 1 anything else
  – Fetch 64-bits/clock cycle; Int on left, FP on right
  – Can only issue 2nd instruction if 1st instruction issues
  – More ports for FP registers to do FP load & FP op in a pair
Type Pipe Stages
Int. instruction IF ID EX MEM WB
FP instruction IF ID EX MEM WB
Int. instruction IF ID EX MEM WB
FP instruction IF ID EX MEM WB
Int. instruction IF ID EX MEM WB
FP instruction IF ID EX MEM WB
1 cycle load delay expands to 3 instructions in SS
  instruction in right half can’t use it, nor instructions in next slot

## Slide 4: Superscalar
IF
IF
ID
ID
IF
IF
EX
EX
ID
ID
IF
IF
M
M
EX
EX
ID
ID
IF
IF
WB
WB
M
M
EX
EX
ID
ID
IF
IF
WB
WB
M
M
EX
EX
ID
ID
WB
WB
M
M
EX
EX
WB
WB
M
M
WB
WB

## Slide 5: Multiple Issue Challenges
Integer/FP split is simple for HW, get CPI of 0.5 only for programs /w:
  Exactly 50% FP operations
  No hazards
If more instructions issue at same time, greater difficulty of decode and issue
  Even 2-scalar => examine 2 opcodes, 6 register specifiers, & decide if 1 or 2 instructions can issue
VLIW: tradeoff instruction space for simple decoding
  The very long instruction word (VLIW) has room for many operations
  By definition, all the operations the compiler puts in the long instruction word are independent  they can be executed in parallel
  E.g., 2 integer operations, 2 FP ops, 2 Memory refs, 1 branch
    16 to 24 bits per field => 7*16 or 112 bits to 7*24 or 168 bits wide
  Need compiling technique that schedules across several branches

## Slide 6: VLIW
Mem. ref. 1 Mem. ref. 2 FP op. 1 FP op. 2 inst branch

## Slide 7: Loop Unrolling in VLIW
Memory Memory FP FP Int. op/ Clock reference 1 reference 2 operation 1 op. 2 branch
LD F0,0(R1) LD F6,-8(R1) 1
LD F10,-16(R1) LD F14,-24(R1) 2
LD F18,-32(R1) LD F22,-40(R1) ADDD F4,F0,F2 ADDD F8,F6,F2 3
LD F26,-48(R1) ADDD F12,F10,F2 ADDD F16,F14,F2 4
ADDD F20,F18,F2 ADDD F24,F22,F2 5
SD 0(R1),F4 SD -8(R1),F8 ADDD F28,F26,F2 6
SD -16(R1),F12 SD -24(R1),F16 7
SD -32(R1),F20 SD -40(R1),F24 SUBI R1,R1,#48 8
SD -0(R1),F28 BNEZ R1,LOOP 9
Unrolled 7 times to avoid delays
7 results in 9 clocks, or 1.3 clocks per iteration (1.8X)
Average: 2.5 ops per clock, 50% efficiency
Note: Need more registers in VLIW (15 vs. 6 in SS)

## Slide 8
Speculation: allow an instruction to issue that is dependent on branch predicted to be taken without any consequences (including exceptions) if branch is not actually taken (“HW undo”); called “boosting”
Combine branch prediction with dynamic scheduling to execute before branches resolved
Separate speculative bypassing of results from real bypassing of results
  When instruction no longer speculative, write boosted results (instruction commit) or discard boosted results
  execute out-of-order but commit in-order to prevent irrevocable action (update state or exception) until instruction commits
HW support for More ILP

## Slide 9: HW support for More ILP
Need HW buffer for results of uncommitted instructions: reorder buffer
  3 fields: instr, destination, value.
  Reorder buffer can be operand source  more registers like RS.
  Use reorder buffer number instead of reservation station when execution completes.
  Supplies operands between execution complete & commit.
  Once operand commits, result is put into register.
  Instructions commit in order.
  As a result, its easy to undo speculated instructions on mispredicted branches or on exceptions.
Reorder
Buffer
FP Regs
FP
Op
Queue
FP Adder
FP Mult
Res Stations
Res Stations

## Slide 10
Load unit

## Slide 11: Four Steps of Speculative Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”)
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW (sometimes called “issue”)
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark reservation station available.
4. Commit—update register with reorder result
  When instr. at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer. Mispredicted branch flushes reorder buffer (sometimes called “graduation”)

## Slide 12
Fetch Unit
Dispatch unit
w/ 8-entry
instruction queue
Register nos.
Data
Cache
Instruction
Cache
Completion
unit w/
reorder
buffer
XSU0
XSU1
MCFXU
LSU
FPU
BPU
Instruction dispatch buses
GP operand buses
Instruction Operation buses
Reorder buffer information
Reservation Stations
GP result buses
Result status buses
Register
nos.
Register nos.
Register nos.
FP operand buses
FP result buses
Branch correction

## Slide 13: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 14: Tomasulo With Reorder buffer:
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 15: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 16: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
5 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 17: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ROB5
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1 10+R2
5 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 18: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
ST 0(R3),F4
ADDD F0,F4,F6
Y
N
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
2 ADDD R(F4),ROB1
6 ADDD M[10],R(F6)
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 19: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 20: Tomasulo With Reorder buffer:
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
What about memory
hazards???
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel