## Slide 1
EE 261, Spring 2025, Lecture 2
Goals/Topics:
Electrical Fundamentals
Current (magnitude & assumed direction)
Voltage (magnitude & assumed polarity)
Power and energy
Some circuit schematic fundamentals: wires and elements
Passive sign convention
Announcements: Homework 0 posted (due Sunday, Jan. 12th).
Homework 1 posted (due Wednesday, Jan. 15th).
Best viewed in presentation mode in PowerPoint.

## Slide 2
Fundamental Concepts:
Matter composed of charged particles (+/–).
Charge can flow.
Charge exerts a force on other charge.
Current is a measure of the rate of flow of charge.
Voltage is a measure of the difference in potential.
Flow of charge through a voltage consumes or delivers
Current.
Voltage.
Familiar with flow of water:
With electrical current:
Amperes, A
Current, i or I
Power.
Charge often represented by or .
fundamental charges (electrons or protons)
(Voltage isn’t a force but
is a measure of potential
that’s related to force.)
(change in potential)

## Slide 3
Current:
Wire representation:
Arrow shows the assumed direction of the flow of positive charge.
Can assume flow in either direction and things always work out.
Units of Amperes, A.
Flows through wires.
or
(rest of circuit not shown)
(rest of circuit not shown)
(or indicated)
(Or through “elements.”)
There isn’t a “right” direction or a “wrong” direction.
Instead, using one direction will yield a positive current while using the opposite direction will yield a negative current.
Only the sign of current depends on assumed direction.
Magnitude of current independent of assumed direction.
Dictated by circuit.

## Slide 4
Current:
Wire representation:
Arrow shows the assumed direction of the flow of positive charge.
Can assume flow in either direction and things always work out.
Charge is not created or destroyed. It only flows.
Charge does not accumulate at any location in (our) circuits.
Units of Amperes, A.
Flows through wires.
or
What flows in must flow out.
(rest of circuit not shown)
(rest of circuit not shown)
(or indicated)
Positive charge flowing in one direction is same as negative charge flowing in opposite direction.
(Or through “elements.”)
}
Equivalent.

## Slide 5
For the wire shown below, the current is .
Thus, the current would be thought of as flowing:
Up.
Down.
If current (positive charge) is moving in indicated direction, current will be positive.

## Slide 6
For the wire shown below, the current is .
If positive charges are flowing, they are moving:
Up.
Down.
Direction of positive charge movement and “direction of current” are synonymous.

## Slide 7
For the wire shown below, the current is .
If negative charges are flowing, they are moving:
Up.
Down.
I don’t want to think about negative charge.
Technically correct.
For this course, (mostly) forget about negative charge.
For historical reasons, we think of current in terms of positive charges.

## Slide 8
Voltage:
Similar to height as measure of potential energy of mass in a gravitational field.
Moving charge from one voltage to another is like moving mass from one height to another. (May require energy or may give up energy.)
Measure of potential energy (of electric charge).
Moving charge from one voltage to another is like moving mass from one height to another.
Gives up energy (delivers power)
Requires energy (consumes power)
Bucket of water
Can also think of voltage as “electric pressure.”
Heights
(top relative to base)
relative to some common reference
relative to some common reference

## Slide 9
Voltage:
Similar to height as measure of potential energy of mass in gravitational field.
Moving charge from one voltage to another is like moving mass from one height to another. (May require energy or may give up energy.)
Measure of potential energy (of electric charge).
Moving charge from one voltage to another is like moving mass from one height to another.
Gives up energy (delivers power)
Requires energy (consumes power)
“Mill”/generator
Pump/motor
Pipe carrying water
Can also think of voltage as “electric pressure.”

## Slide 10
Voltage:
Similar to height as measure of potential energy of mass in gravitational field.
Moving charge from one voltage to another is like moving mass from one height to another. (May require energy or may give up energy.)
Measure of potential energy (of electric charge).
Moving charge from one voltage to another is like moving mass from one height to another.
Gives up energy (delivers power)
Requires energy (consumes power)
Electric charge
Can also think of voltage as “electric pressure.”
Voltages
(difference in potential)
relative to some common reference
relative to some common reference

## Slide 11
Voltage:
Similar to height as measure of potential energy of mass in gravitational field.
Moving charge from one voltage to another is like moving mass from one height to another. (May require energy or may give up energy.)
Measure of potential energy (of electric charge).
Moving charge from one voltage to another is like moving mass from one height to another.
Gives up energy (delivers power)
Requires energy (consumes power)
Load (resistor for example)
Source (voltage or current source)
Wire carrying charge
Can also think of voltage as “electric pressure.”

## Slide 12
Voltage:
Similar to height as measure of potential energy of mass in gravitational field.
Moving charge from one voltage to another is like moving mass from one height to another. (May require energy or may give up energy.)
Movement requires force through a distance.
Work (a.k.a. Energy)
(work) (charge) (voltage)
Voltage, or
Units: Volts,
Measure of potential energy (of electric charge).
Moving charge from one voltage to another is like moving mass from one height to another.
Work often represented by or .
Can also think of voltage as “electric pressure.”
energy “to lift an apple ”
pound

## Slide 13
Voltage always measured between two points.
Often choose (or are given) a reference point in circuit, called “ground,” and assign it a voltage (potential) of zero.
Positive charges wants to move/flow from higher potential to lower.
All points on a wire are at the same potential.
All points on these wires at same voltage.
(Similar to height of something: Height relative to what?)
“element” resistor or voltage source or current source or…
In general, have different voltages to
either side of element.
Perfectly fine to have negative voltages.
(Assuming they are in contact.)
Notes: Chimborazo, Ecuador: Highest point on Earth. Mauna Kea: Tallest mountain.

## Slide 14
Voltage
Circuit elements often presented together with voltage across them.
Sometimes voltages presented as existing at points in a circuit (but these voltages are actually relative to ground/reference point).
“Polarity” is assumed and indicated with plus sign (, higher potential) and minus sign (, lower potential).

## Slide 15
Voltage
Circuit elements often presented together with voltage across them.
Sometimes voltages presented as existing at points in a circuit (but these voltages are actually relative to ground/reference point).
Note:
“Polarity” is assumed and indicated with plus sign (, higher potential) and minus sign (, lower potential).
is voltage “drop” from left side of element to ground.
is voltage “drop” from right side of element to ground.
v1
is voltage drop from left (high) side to right (low) side.
is voltage drop from right side to left side.
Dictated by circuit.
Voltage magnitude independent of polarity. Voltage sign depends on polarity.
Voltage magnitude independent of polarity. Voltage sign depends on polarity.

## Slide 16
The upper wire is at and the lower wire is at .
A positive charge moves from the upper wire to the
lower. This movement:
Requires energy.
Gives up energy.

## Slide 17
The upper wire is at and the lower wire is at .
A positive charge moves from the upper wire to the
lower. This movement:
Requires energy.
Gives up energy.

## Slide 18
The upper wire is at and the lower wire is at .
A negative charge moves from the upper wire to the
lower. This movement:
Requires energy.
Gives up energy.
I don’t want to think about negative charge.
Technically correct.
Again, for this course, (mostly) forget about negative charge.

## Slide 19
Power, or
VA, Watt (),
Power

## Slide 20
Passive Sign Convention
If the (assumed) direction of current is
into the (assumed) higher voltage “terminal” of an element,
the voltage and current are related with a positive sign.
Otherwise use a negative sign.
Power:
Consumed power is positive.
Delivered power is negative.
(Only “relationship” we have now with and is power. Later, will have many more relationships. Passive convention always pertains!)
(Important!)