## Slide 1
EE 261, Spring 2025, Lecture 8
Goals/Topics:
Series resistors
Parallel resistor
“Isolated” circuits with a common ground
Parallel resistors and conductances
More on series and parallel resistors
Announcements: Homework 3 posted. Due Wednesday, Jan. 29th.
Test 1 next Friday, January 31st, at 7:00 p.m. in Spark G45.
Lecture that day will be an optional review.
Best viewed in presentation mode in PowerPoint.

## Slide 2
Series Resistors
Apply Ohm’s Law:
KVL:
where “equivalent resistance” .
Series resistances add.
Long version: Series resistors are equivalent to a single resistor whose resistance equals the sum of the resistances of the resistors that are in series.

## Slide 3
A) Yes. B) No.
Consider:
Does application of Ohm’s Law yield the following?
Does KVL yield the following?
Is equivalent resistance the following?
A) Yes. B) No.
A) Yes. B) No.
Series resistances add.
(Regardless of any labels.)
Minus signs cancel!
passive sign convention

## Slide 4
Arbitrary Number of Series Resistors
Order of resistors does not matter.
where:
Again: Order of series elements does not matter.

## Slide 5
Parallel Resistors
KCL:
Apply Ohm’s Law.
where
Equivalent resistance is the inverse of the sum of the inverses of the
resistances of the resistors in parallel.
Parallel element have same voltage across them.
(Order of resistors does not matter.)

## Slide 6
Ohm’s Law:
Arbitrary Number of Parallel Resistors (Parallel Conductances)
Inverse of resistance is conductance: (mhos, )
Parallel conductances add.
W
Equate denominators.
Ohm’s Law:

## Slide 7
Ohm’s Law:
Arbitrary Number of Parallel Resistors (Parallel Conductances)
Inverse of resistance is conductance: (mhos, )
W
Ohm’s Law:
For a given voltage…
the larger resistance becomes, the smaller the current that flows.
the larger resistance becomes, the smaller conductance becomes.
the smaller conductance becomes, the smaller the current that flows.
the smaller resistance becomes, the larger the current that flows.
the smaller resistance becomes, the large conductance becomes.
the larger conductance becomes, the larger the current that flows.

## Slide 8
Example:
Example:
Example:
Series resistors indicated with “”.
If , , and in series
If , , and in parallel
Parallel resistor indicated with “”.
Example:
Bigger than biggest resistor!
Smaller than smallest resistor!
Important reality checks!
Example:
Common notation related to circuit topology:

## Slide 9
Charge does not accumulate in any portion of circuit.
What flows in flows out. Thus:
HW related:
Bottom wire(s) all at same potential.
(Common ground.)

## Slide 10
Consider:
Are any elements in series?
A) Yes. B) No.
Are any elements in parallel?
A) Yes. B) No.
How to solve for voltages or currents?
One approach: Wye-to-delta or delta-to-wye transformation.
Next lecture…

## Slide 11
Is in series with another resistor?
A) Yes. B) No.
Is in parallel with another resistor?
A) Yes. B) No.
Can an element that is in series with another element ever be in parallel with yet another element?
A) Yes. B) No.
If circuit consists of only two elements, they are simultaneously in series & in parallel.
Consider:
Equivalent resistance ?
Recall elements need not be in series or parallel with any other elements!
E.g. above.

## Slide 12
Consider:
in series with :
in parallel with this combination:
in series with this combination:
in parallel with this combination:
Equivalent resistance ?

## Slide 13
Consider:
Equivalent resistance ?
equal resistors in parallel
Note:

## Slide 14
Consider:
Equivalent resistance ?
Note: and resistors “ended up” in series, but they were always in series.
They must have the same current passing through them. Hence, they’re in series.
Note: and resistors “ended up” in series, but they were always in series.
They must have the same current passing through them. Hence, they’re in series.

## Slide 15
Series:
Parallel:
Recall:
Assuming no resistor is zero or infinite, equivalent resistance of series resistors is always greater than resistance of any single resistor.
Assuming no resistor is zero or infinite, equivalent resistance of parallel resistors is always less than resistance of any single resistor.

## Slide 16
True
False
Is the following true or false?

## Slide 17
True
False
Is the following true or false?
This is true.

## Slide 18
True
False
Is the following true or false?
Product over the sum.

## Slide 19
True
False
Is the following true or false?

## Slide 20
Given:
True
False
Is the following true or false?
Can “replace” pairs of parallel resistors with their equivalents (even while they are in parallel with other resistors).
Can “replace” pairs of parallel resistors with their equivalents
Equal.

## Slide 21
Can measure voltage, current, and resistance (act as an ohmmeter).
But it has its limits…
Attempt to measure resistor.
Parallel
Redraw circuit.
No current through voltmeter.
Combine parallel resistors.
Digital Multimeter (DMM)
DMM being used as an ohmmeter.
DMM
DUT
DUT Device Under Test

## Slide 22
Assume DMM reports resistance at terminals as:
Multiply numerator and denominator by .
Ideally DMM would report just this.
Deviation from is an error.
Ohm’s Law.
DMM
Voltmeter, not a voltage source.

## Slide 23
If
If
If
If
can never be larger than !
Excellent! Almost no error.
Tolerable error?
Ugh! Not good.
Way off!
Ideally, just this.
Deviation from one is an error.