## Slide 1
EE 261, Spring 2025, Lecture 21
Goals/Topics:
Test 2 results
More on inductors
Introduction to capacitors
Announcements: HW 7 posted (due Sunday, March 9th midnight).
And…
Best viewed in presentation mode in PowerPoint.

## Slide 3
Excited by the Aerospace Industry?
We are a satellite engineering club!
We focus on the development and assembly, through launch of CubeSat satellites from start to space!
Electrical Team:
PCB Design
PCB Assembly
Systems Integration
Soldering
Circuit Design
Board creation
Self-starters wanted
Questions? Join our
Microsoft Teams:
Join us in Dana 306!
Meetings Sunday @ 12:30!

## Slide 4
 | Test 1
# of Students | 130
Average | 79.4
Std. Dev. | 15.2
Median | 80
High Score | (18 x) 100
Test 2 Results:
Solution available at Canvas and course website.
If you missed anything, please check out the solution.
B-
Understand your mistakes and learn from them.
 | Test 1 | Test 2
# of Students | 130 | 130
Average | 79.4 | 70.0
Std. Dev. | 15.2 | 16.6
Median | 80 | 68
High Score | (18 x) 100 | (4 x) 100
 | Test 1 | Test 2 | Avg. T1, T2
# of Students | 130 | 130 | 130
Average | 79.4 | 70.0 | 74.7
Std. Dev. | 15.2 | 16.6 | 14.5
Median | 80 | 68 | 75
High Score | (18 x) 100 | (4 x) 100 | (4 x) 100

## Slide 5
Recall: Inductors
Inductors characterized by their inductance, , in henries (H).
Governing - equation:
or
Integrate both sides from time to :
“An inductor is an electrical component that opposes any change in electrical current.”
Note initial condition.
The larger is, the smaller the rate of change in current for a given voltage.

## Slide 6
Inductors
If the current is not changing, an inductor behaves as:
A short circuit
An open circuit
A voltage source
A current source
None of these
But, could be any constant amount.
or
Later we will see that from one instant to the next, can be useful to regard an inductor as akin to a current source (current maintainer).
This relates to inductors “opposing” changes in current.
Schematic representation suggestive of a (coil of) wire, i.e., a short. That’s essential what inductor becomes if current constant.
Current constant.
Schematic representation suggestive of a (coil of) wire, i.e., a short. That’s essential what inductor becomes if current constant.
If the current is not changing

## Slide 7
Inductors
or
Things to note:
If current is not changing, voltage across inductor is zero.
Indistinguishable from a short circuit!
Current cannot change instantaneously.
(Current must change continuously.)
Inductors store energy.
(They can deliver or consume power, but energy is never lost.)
Voltage can change discontinuously/instantaneously.
Important!
(Tends toward open-circuit behavior at high frequencies.)
Why?
Key to finding initial and final conditions in circuits we’ll soon consider.

## Slide 8
Inductor Power and Energy
Stored energy obtained by integrating both sides (from zero to ):
Stored Energy
Power
At an instant of time .
Always non-negative.
At an instant of time .
Positive (consuming) or negative (delivering).

## Slide 9
Capacitors
Store equal and opposite amounts of charge on conducting plates separated by a non-conducting gap.
(No net accumulation of charge!)
Conduction current is flow of actual charges in a conductor.
Displacement current is created by a changing electric field.
Both currents have units of amperes and can be thought of as equivalent in terms of “movement” of charge.
(Maxwell’s great contribution was postulating existence of displacement current.)
(Conduction current exists in wires.)
(Displacement current exists in gap between plates.)

## Slide 10
Capacitors
Circuit representation:
(Don’t worry about curvature of one of the plates. Can draw both as straight.)
iconduction idisplacement
KCL still holds at the circuit level. Net charge isn’t being accumulated anywhere.
KCL still holds at the circuit level. Net charge isn’t being accumulated anywhere.

## Slide 11
Capacitors characterized by their capacitance, C, in farads (F).
Governing - equation:
or
Integrate both sides from time to :
(Could say capacitors “oppose” changes in voltage.)
Recall:
Employ capacitor - relationship.
Note initial condition.
Capacitors

## Slide 12
Capacitors
If the voltage is not changing, a capacitor behaves as:
A short circuit
An open circuit
A voltage source
A current source
Something else
But, could be any constant amount.
Schematic representation is suggestive of an open circuit. That’s essentially what capacitor becomes if voltage constant.
Later we will see that from one instant to the next, can be useful to regard a capacitor as akin to a voltage source (voltage maintainer).
This relates to capacitors “opposing” changes in voltage.
Voltage constant.
Schematic representation is suggestive of an open circuit. That’s essentially what capacitor becomes if voltage constant.
If the voltage is not changing

## Slide 13
Recap: Inductors
Capacitors
representation
in terms of
in terms of
representation
in terms of
in terms of
Include minus sign if current flowing into lower polarity terminal!
Passive sign convention always holds.

## Slide 14
Capacitors
Things to note:
If voltage is not changing, current through capacitor is zero.
Indistinguishable from an open circuit!
Voltage cannot change instantaneously.
(Voltage must change continuously.)
Capacitors store energy.
(They can deliver or consume power, but energy is never lost.)
Current can change discontinuously/instantaneously.
Important!
(Tends toward short-circuit behavior at high frequencies.)
Why?
Key to finding initial and final conditions in circuits we’ll soon consider.

## Slide 15
Capacitor Power and Energy
Stored energy obtained by integrating both sides (from zero to ):
Stored Energy
Power
Never negative.
Negative or positive.