## Slide 1
EE 261, Spring 2025, Lecture 25
Goals/Topics:
RC circuit initial conditions
Voltage division (and some basics) refresher
First-order RC circuit (natural response)
Forced responses
Announcement: Homework 8 due Sunday.
Best viewed in presentation mode in PowerPoint.

## Slide 2
Behaves as an open circuit in steady-state (i.e., when no variation in time).
Recall Capacitors
Important properties:
Voltage cannot change instantaneously.
(“Opposes” changes in voltage.)
(Stores energy.)
Current can change discontinuously/instantaneously.
and
Governing - equations:

## Slide 3
Even if circuit not in steady-state, at any given time, all circuits laws we’ve already learned hold: Ohm’s law, KVL, KCL, etc.
Even if circuit not in steady-state, at any given time, all circuits laws we’ve already learned hold: Ohm’s law, KVL, KCL, etc.
iC = –i1 = –0.5 A
Recall:
Given:
What is ?
(0 A)(20 W) = 0 V
What is ?
i1 = (10 V)/(20 W) = 0.5 A
i1 = (10 V)/(20 W)
What is ? (numeric poll)
Now parallel with & .
10 V
What is ? (numeric poll)
iC = –i1
iC = –(10 V)/(10 W) = –1 A
iC = –(10 V)/(10 W)
May not need to be concerned with details of governing diff. eq. if we’re interested in values at a particular time.
Current changed discontinuously.
Now parallel with & .
Resistors now in parallel:
Ohm’s Law.
Circuit not in steady state at .

## Slide 4
Can you first find current through series combination , then use current to find , then use ? Yes!
Voltage division check-up
What is ? (numeric poll)
Can you solve using KCL? Yes!
Can you solve using KCL? Yes!
Is equal to ?
is voltage across resistor owing to difference in voltage across the series combination.
A) Yes B) No
, , and are node voltages relative to ground.
(high polarity)(low polarity)
Simplest?
Can you first find current through series combination , then use current to find , then use ? Yes!
Can you first find current through series combination , then use current to find , then use ? Yes!
Can you first find current through series combination , then use current to find , then use ? Yes!
is an element voltage.

## Slide 5
RC Circuit: What is ?
Switch is “thrown” at .
What is for ?
.
Voltage can’t change instantly:
For , KCL for and :
RC Circuit
(Assumed in left position “for a long time,” i.e., circuit in steady state prior to switch moving.)
(Note: For , .)
Initial condition.
Not relevant for

## Slide 6
RC Circuit: What is v(t)?
where
and
.
for .
Same form as all first-order circuits.
Time constant always for an “RC” circuit.
Not relevant for
But, also:
for .

## Slide 7
&
&
&
Recap:

## Slide 8
May be given or may have to determine from circuit. Requires some additional information.
May be given or may have to determine from circuit. Requires some additional information.
Comments:
In previous slide, if switches thrown at , replace with with in solution, i.e., replace with .
All are governed by same type of differential equation:
  First-order system with constant coefficients.
  Homogeneous equation (no forcing function) which yields “natural response” of system.
Same solution: exponential decay.
Behavior dictated by constants and initial conditions.
Initial condition: .
Value at time .
Time constant: .
Dictated solely by circuit (i.e., by diff. eq.).

## Slide 9
What about more complicated arrangements of resistors?
Doesn’t matter!
Replace all resistors with single equivalent resistance.
&
Norton equivalent of arbitrary circuit.
Essentially same as before.

## Slide 10
Natural Response (no source present)
What is governing differential equation?
What is initial condition?
What is final condition?
Need additional information.
Circuit dictates.
Forced Response (source present)
(Obtained via KCL at top or bottom nodes or via KVL around right mesh.)
Circuit for
Circuit dictates.
Original circuit can be much more complicated, but inductor merely “sees” Norton equivalent!
Will consider only constant forcing functions (for now).
(Will see that solution only depends on , , , and .)
and hence time constant

## Slide 11
What is governing differential equation?
What is initial condition?
What is final condition?
Need additional information.
Circuit dictates.
Natural Response (no source present)
Forced Response (source present)
(Obtained via KCL at upper right corner or via KVL around mesh.)
Circuit dictates.
Original circuit can be much more complicated, but capacitor merely “sees” Thévenin equivalent!
(Will see that solution only depends on , , , and .)

## Slide 12
Guiding Facts:
Inductor current cannot change instantaneously.
Capacitor voltage cannot change instantaneously.
In steady state:
  Inductor behaves as a short circuit.
  Capacitor behaves as an open circuit.
Notation:
If a switch is thrown at ,
is instant before switch thrown,
is instant after switch thrown.
For inductors, .
For capacitors, .

## Slide 13
Initial conditions: May have to find or may be given.
Assume (or are told) steady state exists prior to any change.
Replace inductor with short and find current through short.
Replace capacitor with an open circuit and find voltage across open.
Final conditions: Independent of initial conditions.
Assume steady state exists after change (and a long time has elapsed).
Replace inductor with short and find current through short.
Replace capacitor with an open circuit and find voltage across open.
Simply find the current (for inductor) or voltage (for capacitor) for what are now purely resistive circuits.
If initial conditions must be found (i.e., are not given):
All analysis techniques we’ve considered are still relevant when solving for these values.

## Slide 14
Note .
Consider: Want .
For , .
KCL at bottom node:
Note .
Assume (given) .
constant
(Forced system, i.e., step response.)
(Not in steady state at .)
(Steady state at .)