## Slide 1
EE 261, Spring 2025, Lecture 36
Goals/Topics:
More circuit fundamentals (sinusoidal steady-state)
More complex number fundamentals (MATLAB tools)
Phasor conversion
Circuit analysis examples
Announcements: Homework 12 due Sunday, Apr. 20th.
Final exam Wednesday, Apr. 30, 1:30 p.m. to 3:30+ p.m. (Fulmer 226).
And…
Best viewed in presentation mode in PowerPoint.

## Slide 3
Recall:
Impedances are just like resistances: ratio of voltage to current.
Series impedances add.
Equivalent of parallel impedances is inverse of sum of inverses.
(Product over sum works for two—and only two— parallel impedances.)
Keep in mind impedances can have positive or negative imaginary parts (and imaginary parts associated with energy storage, not energy consumption).
(in phasor form)
Impedances are just like resistances: ratio of voltage to current.
Keep in mind impedances can have positive or negative imaginary parts (and imaginary parts associated with energy storage, not energy consumption).

## Slide 4
What is equivalent impedance for the following?
A) , B) , C) , D) , E) None of these.
Way in which impedance changes for changes in frequencies key to creating “filters.”
Circuits II
at the that yields these impedances
at the that yields these impedances
Cancel
increases as increases; decreases as decreases.
}
}
increases as increases; decreases as decreases.
decreases as increases; increases as decreases.
decreases as increases; increases as decreases.

## Slide 5
Equivalent Circuits
Any arrangement of sources and impedances can be reduced to a single impedance and a single source.
Thévenin equivalent.
Norton equivalent.

## Slide 6
All the circuit analysis techniques previously considered for resistive circuits with constant sources pertain to ones with impedance and phasors (simply use complex numbers instead of real ones).
KVL, KCL, voltage division, current division, … All the same as before.
Series impedances add.
Parallel impedance combine as inverse of sum of inverses.
Node-voltage and mesh-current analysis: Same as before (but with phasors and impedances, i.e., complex numbers).
(But with complex numbers.)
Recall, for sinusoidal steady state:
Thévenin and Norton equivalent circuits: Same as before (but with phasors and impedances, i.e., complex numbers).

## Slide 7
What is equivalent impedance for the following?
A) , B) , C) , D) , E) None of these.
Parallel combination appears as an open circuit.
Anything in parallel with an open circuit appears as that “anything.”

## Slide 8
N&R Prob. 9.34
At what frequency is in phase with ?
Impedance seen by source must be purely real.
Does resistor factor into solution?
No.
Need equivalent impedance of remaining elements to be purely real.
If impedance is purely real, admittance is purely real.
What frequency makes total admittance real (susceptance zero)?
Following may come in handy:
( must be zero if and have same phase.)
(HW Mastering.)

## Slide 9
Consider:
A) , B) , C) , D) , E) None of these.
Open circuit:
?
?
D
C
In steady state, inductor and capacitor exchange energy, but they do not draw any energy from source. Energy got to inductor and capacitor in a prior transient.
Same as just “” but angle emphasizes this is a phasor.
In steady state, inductor and capacitor exchange energy, but they do not draw any energy from source. Energy got to inductor and capacitor in a prior transient.
Recall Ohm’s Law:
Recall KVL.
In time domain?

## Slide 10
Phasor Transforms:
?
Want a single complex number that gives magnitude and phase of the sum of these two functions.
Recall:
Euler’s formula.

## Slide 11
Phasor Transforms:
Add two terms on right side and express the result in polar form.
Aside: This shows that
?

## Slide 12
rad2deg(angle(12.7555 – 8.6809i))
Example:
What is ?
What is (as a single sinusoid)?
Using MATLAB to add phasors:
and
Recall:
5*exp(j*pi/6) + 14*exp(j*(deg2rad(37) - pi/2))
15.4292
abs(12.7555 – 8.6809i)
12.7555 – 8.6809i
rad2deg(angle(12.7555 – 8.6809i))
-34.2377
5*exp(j*pi/6) + 14*exp(j*(deg2rad(37) - pi/2))
But, want polar form, i.e., .
Aside:
Careful! Mix of radians and degrees.

## Slide 13
Phasor Transforms:
Cannot combine phasors at different frequencies!
Typically the “sign” is incorporated in the phase.
?
All of these are acceptable.

## Slide 14
Consider:
?
Use frequency domain!