## Slide 1: RGB, HSL, HSV
HSL, HSV: easier to define, closer to human vision
http://colorizer.org/

## Slide 2
Lab 2: Movement
Lab 3: Vision

## Slide 3: Classification of Sensors
Proprioceptive sensors
  measure values internally to the system (robot),
  e.g. motor speed, wheel load, heading of the robot, battery status
Exteroceptive sensors
  information from the robots environment
  distances to objects, intensity of the ambient light, unique features.
Passive sensors
  energy coming for the environment
Active sensors
  emit their proper energy and measure the reaction
  better performance, but some influence on envrionment

## Slide 4
What makes a good sensor?
How do you differentiate between sensors?

## Slide 5: Characterizing Sensor Performance (1)
Measurement in real world environment is error prone
Basic sensor response ratings
  Dynamic range
    ratio between lower and upper limits, usually in decibels (dB, power)
    e.g. power measurement from 1 Milliwatt to 20 Watts
    e.g. voltage measurement from 1 Millivolt to 20 Volt
    20 instead of 10 because square of voltage is equal to power
  Range
    upper limit

## Slide 6: Characterizing Sensor Performance (2)
Basic sensor response ratings (cont.)
  Resolution
    minimum difference between two values
    usually: lower limit of dynamic range = resolution
    for digital sensors it is usually the analog-to-digital conversion
      e.g. 5V / 255 (8 bit)
  Linearity
    variation of output signal as function of the input signal
    linearity is less important when signal is after treated with a computer
  Bandwidth or Frequency
    the speed with which a sensor can provide a stream of readings
    usually there is an upper limit depending on the sensor and the sampling rate
    Lower limit is also possible, e.g. acceleration sensor

## Slide 7
Insitu
vs.
in situ

## Slide 8
vs.
in situ
in its original place
"mosaics and frescoes have been left in situ”
in position
"her guests were all in situ"
In the aerospace industry, equipment on-board aircraft must be tested in situ, or in place, to confirm everything functions properly as a system. Individually, each piece may work but interference from nearby equipment may create unanticipated problems.

## Slide 9: In Situ Sensor Performance (1)
Sensitivity
  ratio of output change to input change
  however, in real world environment, the sensor has very often high sensitivity to other environmental changes, e.g. illumination
Cross-sensitivity
  sensitivity to environmental parameters that are orthogonal to the target parameters (e.g., compass responding to building materials)
Error / Accuracy
  difference between the sensor’s output and the true value
m = measured value
v = true value
error

## Slide 10: In Situ Sensor Performance (2)
Characteristics that are especially relevant for real world environments
Systematic error  deterministic errors
  caused by factors that can (in theory) be modeled  prediction
Random error  non-deterministic
  no prediction possible
  however, they can be described probabilistically
Precision
  reproducibility of sensor results
Notes:   e.g. calibration of a laser sensor or of the distortion cause by the optic of a camera
  e.g. Hue instability of camera, black level noise of camera ..

## Slide 11: Characterizing Error: Challenges in Mobile Robotics
Mobile Robot: perceive, analyze and interpret state
Measurements are dynamically changing and error prone
Examples:
  changing illuminations
  specular reflections
  light or sound absorbing surfaces
  cross-sensitivity of robot sensor to robot pose and robot-environment dynamics
    rarely possible to model  appear as random errors
    systematic errors and random errors may be well defined in controlled environment

## Slide 12: Multi-Modal Error Distributions
Behavior of sensors modeled by probability distribution (random errors)
  usually very little knowledge about causes of random errors
  often probability distribution is assumed to be symmetric or even Gaussian
  however, may be very wrong….
    Sonar (ultrasonic) sensor might overestimate the distance in real environment and is therefore not symmetric
    Sonar sensor might be best modeled by two modes: 1. the case that the signal returns directly 2. the case that the signals returns after multi-path reflections
    Stereo vision system might correlate to images incorrectly, thus causing results that make no sense at all…

## Slide 13: Wheel / Motor Encoders (1)
measure position or speed of the wheels
Integrate wheel movements to get an estimate of robots position  odometry
optical encoders are proprioceptive sensors
  position estimation in relation to a fixed reference frame is only valuable for short movements
typical resolutions: 2000 increments per revolution.

## Slide 14: Wheel / Motor Encoders (2)

## Slide 15: Wheel / Motor Encoders (2)

## Slide 16: Wheel / Motor Encoders (3)

## Slide 17: Wheel / Motor Encoders (2)
4.1.3
scanning reticle fields
scale slits
Notice what happen when the direction changes:

## Slide 18: Heading Sensors
Proprioceptive (gyroscope, inclinometer) or Exteroceptive (compass)
Determine the robot’s orientation
Heading + velocity integrates to position estimate
  Dead reckoning (ships)
  Location + Orientation = Pose

## Slide 19: Compass
~2000 B.C.
  Chinese suspended a piece of naturally magnetite from a silk thread and used it to guide a chariot over land
Magnetic field on earth
  absolute measure for orientation
Large variety of solutions to measure the earth magnetic field
Major drawbacks
  weakness of the earth field
  easily disturbed by magnetic objects or other sources
  not feasible for indoor environments

## Slide 20: Gyrocompass
  Patented in 1885
  Practical in 1906 (Germany)
  Find true north as determined by Earth’s rotation
  Not affected by ship’s composition, variety in magnetic field, etc.

## Slide 21: Gyroscope
Heading sensors keep the orientation to a fixed frame
  absolute measure for the heading of mobile system
Mechanical Gyroscopes
  Drift: 0.1° in 6 hours
  Spinning axis is aligned with north-south meridian, earth’s rotation has no effect on gyro’s horizontal axis
  If points east-west, horizontal axis reads the earth rotation
Optical Gyroscopes (1980s)
  2 laser beams in opposite direction
  around circle
  Bandwidth >100 kHz
  Resolution < 0.0001 degrees/hr

## Slide 22: Mechanical Gyroscopes
Concept: inertial properties of a fast spinning rotor
  gyroscopic precession
Angular momentum associated with a spinning wheel keeps the axis of the gyroscope inertially stable.
Reactive torque tao (tracking stability) is proportional to the spinning speed w, the precession speed W and the wheels inertia I.
No torque can be transmitted from the outer pivot to the wheel axis
  spinning axis will therefore be space-stable
Quality: 0.1° in 6 hours
If the spinning axis is aligned with the north-south meridian, the earth’s rotation has no effect on the gyro’s horizontal axis
If it points east-west, the horizontal axis reads the earth rotation

## Slide 23: Rate gyros
Same basic arrangement shown as regular mechanical gyros
But: gimble(s) are restrained by a torsional spring
  enables to measure angular speeds instead of the orientation.
Others, more simple gyroscopes, use Coriolis forces to measure changes in heading.
4.1.4

## Slide 24: Optical Gyroscopes
Early 1980: first installed in airplanes
Angular speed (heading) sensors using two monochromic light / laser beams from same source
On is traveling clockwise, the other counterclockwise
Laser beam traveling in direction of rotation
  slightly shorter path -> shows a higher frequency
  difference in frequency Df of the two beams is proportional to the angular velocity W of the cylinder
New solid-state optical gyroscopes based on the same principle are build using microfabrication technology
MUCH more accurate than mechanical

## Slide 25: Ground-Based Active and Passive Beacons
Beacons are signaling guiding devices with a precisely known positions
Beacon-base navigation is used since the humans started to travel
  Natural beacons (landmarks) like stars, mountains, or the sun
  Artificial beacons like lighthouses
Global Positioning System revolutionized modern navigation technology
  key sensor for outdoor mobile robotics
  GPS not applicable indoors
Major drawback with the use of beacons in indoor:
  Beacons require environment changes: costly
  Limit flexibility and adaptability to changing environments
Key design choice in Robocup
  https://www.youtube.com/watch?v=Kc8ty9mog-I

## Slide 26: Global Positioning System (GPS) (1)
Developed for military use, now commercial
  24 satellites (including some spares)
  Orbit earth every 12 hours at a height of 20.190 km
  Location of GPS receiver determined through time of flight measurement
Technical challenges:
  Time synchronization between individual satellites and GPS receiver
  Real time update of the exact location of the satellites
  Precise measurement of the time of flight
  Interferences with other signals

## Slide 27: Global Positioning System (GPS) (2)
How many satellites do you need to see?
Notes: 3 for position (assume at sea level)
4 for position + time (more accurate)

## Slide 28: Global Positioning System (GPS) (3)
Time synchronization:
  atomic clocks on each satellite, monitored from different ground stations
  electromagnetic radiation propagates at light speed (0.3 m / nanosecond)
  position accuracy proportional to precision of time measurement
Real time update of exact location of satellites:
  Monitoring satellites from a number of widely distributed ground stations
  master station analyses all measurements & transmits actual position to each satellite
Exact measurement of the time of flight:
  quartz clock on the GPS receivers are not very precise
  four satellite allows identification of position values (x, y, z) and clock correction ΔT
Position accuracies down to a ~2 meters
Improvement: Differential GPS
  ~10cm
  Need fixed, known location
  Piski: http://swiftnav.com/piksi.html
  Project possibilities here!

## Slide 29: “Indoor GPS”
If you could set up something on a robot and a bunch of somethings in the environment, how could you localize?
Notes: Received Signal Strength Indication

## Slide 30: “Indoor GPS”
http://www.marvelmind.com/
https://www.youtube.com/watch?v=UMCkqU5k6rg
Sound
Wi-Fi
  RSSI
  fingerprinting
  angle of arrival
  Time of Flight
Notes: Received Signal Strength Indication

## Slide 31: Neato
On-board Room Positioning System (RPS) technology
Maps with only one projector!

## Slide 32: Neato
https://www.researchgate.net/publication/221070323_Vector_field_SLAM

## Slide 33: So Far…
Compass
Wheel encoders
Gyroscope
  v.s. Accelerometer?
GPS
  Beacons
  Sound
  WiFi
  Etc.
Notes: Gyroscope = orientation
Non-rotational. Crystals get stressed under movement, causing voltage
Quantified Self movement
Iphone = accelerometer + compass