## Slide 1
James Irwin
  james.irwin@email.wsu.edu
  Mon 1-5pm
  Tue 1:30-4pm
Amirkhosro Vosughi
  amirkhosro.vosughi@email.wsu.edu
  Mostly grading, will have some office hours

## Slide 2: IEEE Spectrum: Dutch Police Training Eagles to Take Down Drones

## Slide 3
Robot Position: ξI=[xI,yI,θI]T
Mapping between frames
ξR=R(θ)ξI
R(θ)=
l: distance from wheel to center of rotation
r: radius of a wheel
ξI=R(θ)-1ξR
Notes: Write out E^dot_R = Rmatix E^dot_I

## Slide 4
ξI=R(θ)-1ξR
l: distance from wheel to center of rotation
r: radius of a wheel

## Slide 5: Example 3/3
A Create robot has wheels with a 5 cm radius which are 30 cm apart. Both wheels rotating forward at 1 rad per second. What are[xR,yR,θR]T in m/s and rad/s? What are[xI,yI,θI]T in m/s and rad/s?

## Slide 6: Worked problem

## Slide 7: Sliding constraint
Standard wheel has no lateral motion
Move in circle whose center is on “zero motion line” through the axis
Instantaneous Center of Rotation

## Slide 8: More complex
Steered standard wheel
Caster wheel
More parameters

## Slide 9: Differential drive
Rotation not constrained
Can move in any circle it wants to
Easy to move around

## Slide 10: Mobile Robot Locomotion
Instantaneous center of rotation (ICR) or Instantaneous center of curvature (ICC)
  A cross point of all axes of the wheels

## Slide 11: Degree of Mobility
# degrees of freedom of robot chassis that can be immediately manipulated through changes in wheel velocity
Degree of mobility : 0
Degree of mobility : 2
Degree of mobility : 3
Degree of mobility : 1
Cannot move anywhere (No ICR)
Fixed arc motion (Only one ICR)
Variable arc motion (line of ICRs)
Fully free motion
(ICR can be located at any position)
Notes: Zero motion line
Instantaneous Center of Rotation
Ackerman steering (car) vs bicycle: same degree of mobilitiy & ICR
2nd steering wheel of car isn’t independent

## Slide 12: Degree of Steerability
The number of centered orientable wheels that can be steered independently in order to steer the robot
Indirect impact on robot chassis pose
Degree of steerability : 0
Degree of steerability : 2
Degree of steerability : 1
No centered orientable wheels
One centered orientable wheel
Two mutually dependent centered orientable wheels
Two mutually independent centered orientable wheels

## Slide 13: Degree of Maneuverability
Degree of Mobility 3 2 2 1 1
Degree of Steerability 0 0 1 1 2
The overall degrees of freedom that a robot can manipulate:
Examples of robot types (degree of mobility, degree of steerability)

## Slide 14: Degree of Maneuverability
Notes: # degrees of freedom robot can manipulate
2: ICR is on a line
3: ICR can be anywhere

## Slide 15
There is no ideal drive configuration that simultaneously maximizes stability, maneuverability, and controllability
Example: typically inverse correlation between controllability and maneuverability

## Slide 16: Holonomic Robots
Holonomic kinematic constraint can be expressed as explicit function of position variables only
Non-holonomic constraint requires addition information
Fixed/steered standard wheels impose non-holonomic constraints

## Slide 17: Holonomicity
If the controllable degrees of freedom is equal to the total degrees of freedom then the robot is said to be holonomic
  Holonomic constraints reduce the number of degrees of freedom of the system
If the controllable degrees of freedom are less than the total degrees of freedom it is non-holonomic
A robot is considered to be redundant if it has more controllable degrees of freedom than degrees of freedom in its task space

## Slide 18: Why study holonomic constraints?
How many independent motions can our turtlebot robot produce?
  2 at the most
How many DOF in the task space does the robot need to control?
  3 DOF
The difference implies that our system has holonomic constraints

## Slide 19: Non-holonomic constraint
So what does that mean? Your robot can move in some directions (forward
and backward), but not others (sideward)
The robot can instantly
move forward and backward,
but can not move sideward
Parallel parking,
Series of maneuvers
A non-holonomic constraint is a constraint on the feasible velocities of a body

## Slide 20: Kinematic model for car-like robot
Control Input
Driving type: Forward wheel drive
X
Y


: forward vel
: steering vel

## Slide 21: Kinematic model for car-like robot
X
Y


non-holonomic constraint:
: forward velocity
: steering velocity

## Slide 22: Dynamic Model
X
Y


Dynamic model

## Slide 23
Open loop control vs. Closed loop control
Car’s cruse control

## Slide 25: The World consists of...
Obstacles
  Places where the robot can’t (shouldn’t) go
Free Space
  Unoccupied space within the world
  Robots “might” be able to go here
    There may be unknown obstacles
    The state may be unreachable

## Slide 26: Configuration Space (C-Space)
Configuration Space: the space of all possible robot configurations.
  Data structure that allows us to represent occupied and free space in the environment

## Slide 27: Configuration Space
For a point robot moving in 2-D plane, C-space is
qgoal
qinit
C
Cfree
Cobs
Point robot (no constraints)

## Slide 28: What if the robot is not a point?

## Slide 29
Expand obstacle(s)
Reduce robot
What if the robot is not a point?

## Slide 30: What if we want to preserve the angular component?

## Slide 31: If we want to preserve the angular component…

## Slide 32: Rigid Body Planning

## Slide 33: Transfer in Reinforcement Learning via Shared Features: Konidaris, Scheidwasser, and Barto, 2012

## Slide 36
Open loop control vs. Closed loop control
Recap
  Control Architectures
  Sensors & Vision
  Control & Kinematics
Notes: https://vid.me/UJSI