## Slide 1: Degree of Maneuverability
Notes: # degrees of freedom robot can manipulate
2: ICR is on a line
3: ICR can be anywhere

## Slide 2
Expand obstacle(s)
Reduce robot
What if the robot is not a point?

## Slide 3: Implementation of a Gaussian process-based machine learning grasp predictor. Goins, Carpenter, Wong, & Balasubramanian, 2015
With the goal of advancing the state of automatic robotic grasping, we present a novel approach that combines machine learning techniques and physical validation on a robotic platform to develop a comprehensive grasp predictor. After collecting a large grasp sample set (522 grasps), we first conduct a statistical analysis of the predictive ability of grasp quality metrics that are commonly used in the robotics literature. We then apply principal component analysis and Gaussian process (GP) algorithms on the grasp metrics that are discriminative to build a classifier, validate its performance, and compare the results to existing grasp planners. The key findings are as follows: (i) several of the existing grasp metrics are weak predictors of grasp quality when implemented on a robotic platform; (ii) the GP-based classifier significantly improves grasp prediction by combining multiple grasp metrics to increase true positive classification at low false positive rates; (iii) The GP classifier can be used generate new grasps to improve bad grasp samples by performing a local search to find neighboring grasps which have improved contact points and higher success rate.

## Slide 5: Manipulators

## Slide 6: Manipulators

## Slide 7: Manipulators

## Slide 8: Manipulation
What is a manipulator?
  Manipulates something in the world
    Physically alter the world through contact
    As a primary goal
    But not its own position
When is this desirable?
  Dangerous workspaces
    Space; foundries; underwater; factories
  Dirty
  Dull Boring, repetitive, unpleasant work
  Human-intractable workspaces
    Too small; too big; too much precision needed
Notes: Ben’s work: moving & opening cabinet

## Slide 9
Current
  Industrial
    Welding
    Drilling
    Attaching (screws, rivets)
    Painting
    Loading/unloading
  Surgery
  Space exploration
  Chores
  Patient care
  Delivery
Future
  Elder care
  Entertainment
  Environment sampling
  Compliant-material interactions (sewing)
  Battery changing
  Police work
Plus: more chores, more patient care, more surgery, more space, &c. (but better)
Davinci
Robot

## Slide 10: Terminology
Actuator
  Generates motion or force; usually a motor
  “Drive type”
DoFs
End Effector
  Device at the end of an arm; interacts with environment
Gripper
  What it sounds like: a type of manipulator

## Slide 11: Manipulator Robot
Modeled as a chain of rigid links connected by joints
Links: unjointed length of robot
Joints: translational or rotational movement
  Joints have DoFs
  Sliding or jointed
Manipulator / End Effectors
  Grippers / Tools
  Sensors
Links
Joints
End Effector (gripper)

## Slide 12: Characterization
Types
  By drive
  By actuation
    Tendons
    Direct servoing
    Underactuation
  By motion
    Prismatic (linear)
    Revolute (rotational)
  By Characteristics
    Payload
    Working area/radius
Notes: Underactuation is a technical term used in robotics and control theory to describe mechanical systems that cannot be commanded to follow arbitrary trajectories in configuration space.
A standard automobile is underactuated due to the nonholonomic constraints imposed by the wheels. That is, a car cannot accelerate in a direction perpendicular to the direction the wheels are facing. A similar argument can be made for boats, planes and most other vehicles.

## Slide 13: Joints
Prismatic: sliding / translational
Revolute: rotational

## Slide 14: Actuators
Hydraulic Motor
Stepper Motor
Pneumatic Motor
Servo Motor
Pneumatic Cylinder
DC Motor

## Slide 15
DC vs. servo motor
  https://www.youtube.com/watch?v=mSowgNx5u7I
Pneumatic vs. Hydraulic
  http://machinedesign.com/linear-motion/what-s-difference-between-pneumatic-hydraulic-and-electrical-actuators

## Slide 16: When Do We Use…
Hydraulic/pneumatic
  Heavy loads, high speeds
  Sometimes hard to control (esp. pneumatic)
  Doesn’t produce sparks
Hydraulic Motor
Pneumatic Motor
Pneumatic Cylinder

## Slide 17: When Do We Use…
Most common robotic actuators: combinations of different electro-mechanical devices
  Stepper motor
    Subdivides a rotation into # increments
    Open Loop
  Servo Motor
    Subdivides a rotation arbitrarily
    Closed Loop
Notes: The servo motor is actually an assembly of four things: a normal DC motor, a gear reduction unit, a position-sensing device (usually a potentiometer—a volume control knob), and a control circuit.
Stepper motors have some inherent ability to control position, as they have built-in output steps.
A servomotor consumes power as it rotates to the commanded position but then the servomotor rests. Stepper motors run warm to the touch because they continue to consume power to lock in and hold the commanded position.
Therefore, on first power up, the controller will have to activate the stepper motor and turn it to a known position, e.g. until it activates an end limit switch. This can be observed when switching on an inkjet printer; the controller will move the ink jet carrier to the extreme left and right to establish the end positions.
The lack of feedback of a stepper motor limits its performance, as the stepper motor can only drive a load that is well within its capacity, otherwise missed steps under load may lead to positioning errors and the system may have to be restarted or recalibrated.
There has been increasing popularity in closed loop stepper motors in recent years. They act like servomotors but have some differences in their software control to get smooth motion.

## Slide 18: Manipulation Configurations & Grasping

## Slide 19: Manipulation Configurations & Grasping

## Slide 20: P(rismatic) & R(evolute)
A kinematic chain of rigid links connected by joints
  “Kinematics is the branch of classical mechanics which describes the motion of objects and groups of objects.”
Prismatic (denoted P)
  Sliding / translational / linear; allows a linear relative motion between 2 links
Revolute (denoted R)
  Rotational; allows relative rotation between two links
Spong, Hutchinson, Vidyasagar. Robot Modeling and Control. 2006.
Notes: REPRESENTING JOINTS

## Slide 21: Joints: Denotation
A joint represents a connection between two links
Denotation of relative displacement between links
  θ for revolute joint
  d for prismatic joint
Denotation of axis of motion
  zi between link i and link i+1
    Axis of rotation of a revolute joint
    Axis of translation of a prismatic joint
Spong, Hutchinson, Vidyasagar. Robot Modeling and Control. 2006.
Notes: Kinematics is the branch of classical mechanics which describes the motion of points, bodies (objects) and systems of bodies (groups of objects) without consideration of the causes of motion. Kinematics as a field of study is often referred to as the "geometry of motion".

## Slide 22: Configuration Space
Configuration
  Specification of location of every point on manipulator.
How can we specify?
  Links are rigid
  Base is (assumed to be) fixed
  So if we know values for the joint variables
    Angle for R joints (θ), offset for P joints (d)
  We know everything!
Manip. configuration ≣ a set of values for joint variables
Set of all possible configurations is the configuration space.
Spong, Hutchinson, Vidyasagar. Robot Modeling and Control. 2006.
Links
Base
Notes: Kinematics is the branch of classical mechanics which describes the motion of points, bodies (objects) and systems of bodies (groups of objects) without consideration of the causes of motion. Kinematics as a field of study is often referred to as the "geometry of motion".

## Slide 23: DoFs for Manipulation
A system has n DoFs if exactly n parameters are required to completely specify the configuration.
For a manipulator:
  Configuration can be specified by n joint parameters, so
  # of DoFs = dimension of the configuration space
  So, # number of joints determines DoFs
Rigid object in 3D space has six parameters
  3 positioning (x, y, z), 3 orientation (roll, pitch and yaw angles)
DoFs < 6 ⇒ arm cannot reach every point in workspace with arbitrary orientation.
Spong, Hutchinson, Vidyasagar. Robot Modeling and Control. 2006.
Notes: Kinematics is the branch of classical mechanics which describes the motion of points, bodies (objects) and systems of bodies (groups of objects) without consideration of the causes of motion. Kinematics as a field of study is often referred to as the "geometry of motion".

## Slide 24: Notes on DoFs
DoFs < 6 ⇒ arm cannot reach every point in workspace with arbitrary orientation
Sometimes you need more
  E.g., dealing with obstacles
DoFs > 6 is kinematically redundant
Difficulty of control problem as # DoFs grows
  Increases rapidly with the number of links
  Every 2 links need a joint
Spong, Hutchinson, Vidyasagar. Robot Modeling and Control. 2006.
Ehsan Rezapour. Pettersen, Gravdahl, Liljebäck, Kelasidi. Robotics and Biomimetics. 2014.
Notes: Kinematics is the branch of classical mechanics which describes the motion of points, bodies (objects) and systems of bodies (groups of objects) without consideration of the causes of motion. Kinematics as a field of study is often referred to as the "geometry of motion".

## Slide 25: Workspaces
Configuration only provides geometry
Workspace
  Set of all possible positions of end effector
  In practice, these can be complex
Dexterous workspace
  Set of points where end effector can be any orientation
  Subset of workspace
Spong, Hutchinson, Vidyasagar. Robot Modeling and Control. 2006.
engineerjau.wordpress.com/2013/07/07/on-the-basis-of-workspaces-of-robotic-manipulators-part-1

## Slide 26: Grippers
Four categories of robot grippers:
  Impactive
    Jaws or claws which physically grasp by direct impact upon the object
  Ingressive
    Pins, needles or hackles penetrate surface
      Textile, carbon and fiberglass handling
  Astrictive
    Suction forces applied to surface
    Vacuum, magneto- or electroadhesion
  Kontugutive / Contigutive
    Requiring direct contact for adhesion
    Glue, surface tension or freezing
Monkman, Hesse, Steinmann, Schunk. Robot Grippers. 2007.
news.nationalgeographic.com/news/2009/05/090505-robot-hand-picture.html
grasping

## Slide 27: Universal Gripper: Video
https://www.youtube.com/watch?v=0d4f8fEysf8
https://www.youtube.com/watch?v=KBTrtQQKl7o

## Slide 28: Grasps
Grasp:
  A set of contact points on an object’s surface
  Goal: constrain object’s movement
www.intechopen.com/books/robot-arms/robotic-grasping-of-unknown-objects1
news.nationalgeographic.com/news/2009/05/090505-robot-hand-picture.html

## Slide 29: Grasps
www.madry.pro
León, Morales, Sancho-Bru. Robot Grasping Foundations. 2013
Grasps vary by:
  Hand (gripper)
  Object being grasped
  Type of motion desired
For each hand or hand/object pair:
  Where to grasp it?
  How hard?
  Then what?
Additional constraints (e.g., don’t spill)
Drinking

## Slide 30: The Grasping Problem
Grasps are not obvious (easy to calculate)
  Any given object has arbitrary contact points
  Hand has geometry constraints, etc.
Synthesized trial-and-error
  For a hand/object pair:
  Different grasp types planned and analyzed
Real trial and error
www.cs.columbia.edu/~cmatei/graspit/
www.programmingvision.com/research.html
www.cc.gatech.edu/gvu/people/faculty/nancy.pollard/grasp.html

## Slide 31: Grasp Planning
Grasp synthesis: Find suitable set of contacts, given
  Object model
  Constraints on allowable contacts
Grasp points are determined
  Mostly assume point contacts
  Larger areas usually discretized
  Contact model defines the force the manipulator exerts on contact areas
Grasp analysis
  Is that grasp stable?
León, Morales, Sancho-Bru. Robot Grasping Foundations. 2013.
www.intechopen.com/books/robot-arms/robotic-grasping-of-unknown-objects1

## Slide 32: Ongoing Research
How do you get the object model?
What are the constraints?
Background knowledge, mathematical modeling, …
www.madry.pro
www.cs.washington.edu/robotics/3d-in-hand

## Slide 33
  https://www.youtube.com/watch?v=rJAti2ymAnY

## Slide 34: Implementation of a Gaussian process-based machine learning grasp predictor. Goins, Carpenter, Wong, & Balasubramanian, 2015
With the goal of advancing the state of automatic robotic grasping, we present a novel approach that combines machine learning techniques and physical validation on a robotic platform to develop a comprehensive grasp predictor. After collecting a large grasp sample set (522 grasps), we first conduct a statistical analysis of the predictive ability of grasp quality metrics that are commonly used in the robotics literature. We then apply principal component analysis and Gaussian process (GP) algorithms on the grasp metrics that are discriminative to build a classifier, validate its performance, and compare the results to existing grasp planners. The key findings are as follows: (i) several of the existing grasp metrics are weak predictors of grasp quality when implemented on a robotic platform; (ii) the GP-based classifier significantly improves grasp prediction by combining multiple grasp metrics to increase true positive classification at low false positive rates; (iii) The GP classifier can be used generate new grasps to improve bad grasp samples by performing a local search to find neighboring grasps which have improved contact points and higher success rate.